## Slide 1: Polarized Electron Beams In The MEIC Collider Ring At JLab
Fanglei Lin
Center for Advanced Studies of Accelerators (CASA), Jefferson Lab
2013 International Workshop on Polarized Sources, Targets & Polarimetry
University of Virginia, Charlottesville, Virginia
September 9th – 13th, 2013
Notes: Title Page

## Slide 2: Outline
Medium-energy Electron Ion Collider (MEIC) at JLab
Introduction to electron spin and polarization, SLIM algorithm and spin matching
Electron polarization design for MEIC: spin rotator, polarization configurations
Example of polarization (lifetime) calculation for MEIC electron collider ring
Summary and perspective

## Slide 3: Future Nuclear Science at Jlab: MEIC
Pre-booster
Ion linac
IP
IP
MEIC
Full Energy EIC
CEBAF

## Slide 4: MEIC Layout
Cross sections of tunnels for MEIC
Warm large booster
(up to 20 GeV/c)
Warm 3-12 GeV
electron collider ring
Medium-energy IPs with
horizontal beam crossing
Injector
12 GeV CEBAF
Prebooster
SRF linac
Ion
source
Cold 20-100 GeV/c
proton collider ring
Three Figure-8 rings
stacked vertically
Hall A
Hall B
Hall C

## Slide 5: Stacked Figure-8 Rings
Interaction point locations:
Downstream ends of the electron straight sections to reduce synchrotron radiation background
Upstream ends of the ion straight sections to reduce residual gas scattering background
Electron Collider
Interaction Regions
Electron path
Ion path
Large Ion Booster
Ion Collider
Vertical stacking for identical ring circumferences
Ion beams execute vertical excursion to the plane of the electron orbit for enabling a horizontal crossing, avoiding electron synchrotron radiation and emittance degradation
Ring circumference: 1400 m
Figure-8 crossing angle: 60 deg.

## Slide 6: MEIC Design Parameters
Energy (bridging the gap of 12 GeV CEBAF and HERA/LHeC)
  Full coverage of s from a few 100 to a few 1000 GeV2
  Electrons 3-12 GeV, protons 20-100 GeV, ions 12-40 GeV/u
Ion species
  Polarized light ions: p, d, 3He, and possibly Li
  Un-polarized light to heavy ions up to A above 200 (Au, Pb)
Up to 2 detectors
  Two at medium energy ions: one optimized for full acceptance, another for high luminosity
Luminosity
  Greater than 1034 cm-2s-1 per interaction point
  Maximum luminosity should optimally be around √s=45 GeV
Polarization
  At IP: longitudinal for both beams, transverse for ions only
  All polarizations >70% desirable
Upgradeable to higher energies and luminosity
  20 GeV electron, 250 GeV proton, and 100 GeV/u ion
arXiv:1209.0757

## Slide 7: MEIC Electron Polarization
Requirements:
  polarization of 70% or above
Strategies:
  highly longitudinally polarized electron beams are injected from the CEBAF (~15s)
  polarization is designed to be vertical in the arc to avoid spin diffusion and longitudinal at collision points using spin rotators
  new developed universal spin rotator rotates polarization in the whole energy range (3-12GeV)
  desired spin flipping can be implemented by changing the polarization of the photo-injector driver laser at required frequencies
  rapid and high precision Mott and Compton polarimeters can be used to measure the electron polarization at different stages
  figure 8 shape facilitates stabilizing the polarization by using small fields
  longitudinal polarization at IPs
  spin flipping
  spin
  spin
  spin
  spin
  Alternating polarization of electron beam bunches
  Illustration of polarization orientation

## Slide 8: Electron Spin And Polarization Equations
Thomas-Bargmann-Michel-Telegdi (Thomas-BMT) equation
Derbenev –Kondratenko Formula (Sokolov-Ternov self-polarization + spin-orbit coupling depolarization)
Polarization build-up rate (the inverse polarization lifetime constant)
    is a 1-turn periodic unit 3-vector field over the phase space satisfying the Thomas-BMT equation along particle
    trajectories ( is not ). Depolarization occurs in general if the spin-orbit coupling function no longer vanishes
    in the dipoles (where is large).
Time-dependent polarization
Notes: A very small fraction of the radiation photons cause spin flip. It is a pure quantum effect associated with disparity of transition rates for spins to flip from along the direction of the dipole field to against the direction of the field and vice versa. The rates differ and this leads to a build-up of electron spin polarization antiparallel to the magnetic field. Positrons become polarized parallel to the field. Baier and Katkov generalized the original S-T expression to an arbitrary magnetic field.
The stochastic element of photon emission together with damping determines the equilibrium phase space density distribution. The same photon emission also impacts a stochastic element to the spin precession, via T-BMT equation, spin diffusion can occur. The spin-orbit coupling function quantifies the radiative depolarization.
The polarization (time) is the result of a balance between the Sokolov-Ternov effect (time) and the radiative depolarization (time). In the approximation that the orbital motion is linear, the value of polarization is essentially the same at each point in phase space and azimuth and the polarization is aligned along the Derbenev-Kondratenko vector --- invariant spin field 𝑛 ̂, which is 1-turn periodic unit 3-vector field over the phase space satisfying the Thomas-BMT equation along particle trajectories, 𝑛 ̂_0is for the particle in the designed orbit.
𝑃_(𝑒𝑛𝑠,𝑑𝑘)=𝑃_𝑑𝑘 ⟨𝑛 ̂ ⟩_𝑠 is the value of ensemble average of 𝑃_𝑑𝑘, the equilibrium polarization along the 𝑛 ̂, which is essentially independent of s.
<>s denotes an average over phase space at azimuth s, s_hat is the direction of motion, b_hat is the magnetic field direction if the electric field vanishes and the motion is perpendicular to the magnetic field.
(𝜕𝑛 ̂)/𝜕𝛿 in the numerator is the so–called kinetic polarization term. This results from the dependence of the radiation power on the initial spin direction and is not associated with spin flip.
(𝜕𝑛 ̂)/𝜕𝛿 includes both transverse motion and synchrotron motion dependence of stable spin direction (or invariant spin field). (𝜕𝑛 ̂_0)/𝜕𝛿 can be approximate synchrotron motion dependence of stable spin direction.

## Slide 9: SLIM Algorithm And Spin Matching
Obtaining expression for in a linear approximation of orbit and spin motion. Therefore, .
The combined linear orbit and spin motion is propagated by an 8x8 transport matrix of
(, ) ()
is a symplectic matrix describing orbital motion; represents no spin effect to the orbital motion;
describes the coupling of the spin variables (, ) to the orbit motion. matrix is the target of so-called
“spin matching”, involving adjustment of the optical state of the ring to make some crucial regions
spin transparent.
is a rotation matrix associated with describing the spin motion in the periodic reference frame.
The code SLICK, created and developed by Prof. A.W. Chao and Prof. D.P. Barber, calculates the equilibrium polarization and depolarization time using SLIM algorithm.
Notes: We understand those terminologies of electron polarization quantitatively. Now we need to describe (or estimate) the electron polarization quantitatively. Two classes of computer algorithm for estimating the equilibrium polarization and lifetime: i) methods on evaluating (𝜕𝑛 ̂)/𝜕𝛿 in the D-K formula given the ring layout and magnet strengths; ii) algorithm using Monte-Carlo tracking.
Class i) methods are further divided according the degree of linearization of the spin and orbit motion, SLIM family (linearization of orbital and pin motion), SMILE (linearized orbital motion but nonlinear spin motion), SPRINT (linearized orbital motion but nonlinear spin motion). Here I briefly introduce the SLIM algorithm created by Dr. Alex Chao and Dr. Desmond Barber, which is used widely for the estimation of electron polarization under the linearization scale for the first step of polarization studies, of course here for MEIC.

## Slide 10: Universal Spin Rotator (USR)
Schematic drawing of USR
Parameters of USR for MEIC
Illustration of step-by-step spin rotation by a USR
E | Solenoid 1 |  | Arc Dipole 1 | Solenoid 2 |  | Arc Dipole 2
 | Spin Rotation | BDL | Spin Rotation | Spin Rotation | BDL | Spin Rotation
GeV | rad | T·m | rad | rad | T·m | rad
3 | π/2 | 15.7 | π/3 | 0 | 0 | π/6
4.5 | π/4 | 11.8 | π/2 | π/2 | 23.6 | π/4
6 | 0.62 | 12.3 | 2π/3 | 1.91 | 38.2 | π/3
9 | π/6 | 15.7 | π | 2π/3 | 62.8 | π/2
12 | 0.62 | 24.6 | 4π/3 | 1.91 | 76.4 | 2π/3
P. Chevtsov et al., Jlab-TN-10-026
IP
Arc

## Slide 11: Solenoid Decoupling Schemes --- LZ Scheme
Litvinenko-Zholents (LZ) Scheme*
  A solenoid is divided into two equal parts
  Normal quadrupoles are placed between them
  Quad strengths are independent of solenoid strength
Half Sol.
5 Quads. (3 families)
Half Sol.
1st Sol. + Decoupling Quads
Dipole Set
2nd Sol. + Decoupling Quads
Dipole Set
Half
Solenoid
Half
Solenoid
Quad. Decoupling Insert
* V. Litvinenko, A. Zholents, BINP (Novosibirsk) Prepring 81-80 (1981). English translation: DESY Report L-Trans 289 (1984)
Notes: With a proper choice of quadrupole strengths, the 4x4 transport matrix for the whole block (half sole. + insert + half sole.) is block diagonalized. The chosen one uses 5 quadrupoles and arranges in a symmetric way (3 families).
The lattice was also optimized by suppressing the dispersion only inside of dipoles sets in the spin rotator, without leaking to the solenoids. This will significantly reduce the depolarization effect to spin-orbit coupling function (𝜕𝑛 ̂)/𝜕𝛿 through the synchrotron motion inside of the solenoids, and consequent demanding in the spin matching

## Slide 12: Solenoid Decoupling Schemes --- KF Scheme
Kondratenko-Filatov (KF) Scheme*
  Mixture of different strength and length solenoids
  Skew quadrupoles are interleaved among solenoids
  Skew quad strengths are dependent of solenoid strengths
1st Sol.
Dipole Set
Decoupling Skew Quads
2nd Sol.
Dipole Set
1st
Solenoid
2nd
Solenoid
Skew Quad.
* Yu. N. Filatov, A. M. Kondratenko, et al. Proc. of 20th Int. Symp. On Spin Physics (DSPIN2012), Dubna.
1st
Solenoid
2nd
Solenoid
3rd
Solenoid
Skew Quad.
..………..

## Slide 13: Polarization Configuration I
Same solenoid field directions in two spin rotators in the same IR (flipped spin in two half arcs )
S-T
FOSP
  FOSP : First Order Spin Perturbation from non-zero δ in the solenoid through G matrix.
spin orientation
  Magnetic field
  Spin vector
Arc
Arc
IP
Solenoid field
Solenoid field
  S-T : Sokolov-Ternov self-Polarization effect
Notes: Interior Page

## Slide 14: Polarization Configuration II
Opposite solenoid field directions in two spin rotators in the same IR (same spin in two half arcs)
S-T
FOSP
  Magnetic field
  Spin vector
spin orientation
  FOSP : First Order Spin Perturbation from non-zero δ in the solenoid through G matrix.
  S-T : Sokolov-Ternov self-Polarization effect
Arc
Arc
IP
Solenoid field
Solenoid field
Notes: Interior Page

## Slide 15: Example Calculation (Polarization Lifetime)1
Polarization configuration I --- (same solenoid field directions)
Energy (GeV) | Equi. Pol.2 (%) | Total Pol. Time2 (s) | Spin-Orbit Depolarization Time (s) |  |  |  | Sokolov-Ternov Polarization Effect |  | Spin Tune4
 |  |  | Mode I3 | Mode II3 | Mode III3 | Subtotal | Pol. (%) | Time (s) | 
5 | 12.4 | 2950 | 86492 | 9E17 | 3954 | 3470 | 87.2 | 19673 | 0.389892
9 | 24.2 | 313 | 1340 | 2E15 | 535 | 449 | 87.6 | 1035 | 0.234249
Energy (GeV) | Equi. Pol.2 (%) | Total Pol Time2 (s) | Spin-Orbit Depolarization Time (s) |  |  |  | Sokolov-Ternov Depolarization Effect |  | Spin Tune4
 |  |  | Mode I3 | Mode II3 | Mode III3 | Subtotal | Pol. (%) | Time (s) | 
5 | 0 | 10178 | 25911 | 6E18 | 84434 | 21086 | 0 | 19673 | 0
9 | 0 | 584 | 1383 | 1E15 | 5123 | 1340 | 0 | 1035 | 0
Polarization configuration II --- (opposite solenoid field directions)
Thick-lens code SLICK was used for those calculations without any further spin matching.
Equilibrium polarization and total polarization time are determined by the spin-orbit coupling depolarization effect and Sokolov-Ternov effect.
Mode I, II, III are the horizontal, vertical and longitudinal motion, respectively, for an orbit-decoupled ring lattice.
Non-zero spin tune in the configuration I is only because of the non-zero integral of the solenoid fields in the spin rotators; non-zero spin tune in the configuration II can be produced by very weak solenoid fields in the region having longitudinal polarization.

## Slide 16: Comparison Of Two Pol. Configurations
Polarization Configuration I same solenoid field directions in the same IR | Polarization Configuration II opposite solenoid field directions in the same IR
Sokolov-Ternov effect may help to preserve one polarization state with spin matching. Spin matching is demanding to maintain the polarization due to the non-zero integral of longitudinal solenoid fields in the two spin rotators in the same IR. The total depolarization time is determined by the spin-orbit coupling depolarization time. Design-orbit spin tune () is not zero, only because of the non-zero integral of longitudinal fields. | Sokolov-Ternov effect does not contribute to preserve the polarization. Spin matching is much less demanding due to the zero integral of longitudinal solenoid fields in the two spin rotators in the same IR. The total polarization time is mainly determined by the Sokolov-Ternov depolarization time. Design-orbit spin tune () is zero, but can be adjusted easily using weak fields because of figure-8 shape.
Polarization Configuration I same solenoid field directions in the same IR | Polarization Configuration II opposite solenoid field directions in the same IR

## Slide 17: Summary And Perspective
Highly longitudinally polarized electron beam is desired in the MEIC collider ring to meet the physics program requirements.
Polarization schemes have been developed, including solenoid spin rotator, solenoid decoupling schemes, polarization configurations.
Polarization lifetimes at 5 and 9GeV are sufficiently long for MEIC experiments.
Future plans:
  Study alternate helical-dipole spin rotator considering its impacts (synchrotron radiation and orbit excursion) to both beam and polarization
  Study spin matching (linear motion) schemes and Monte-Carlo spin-obit tracking with radiation (nonlinear motion)
  Consider the possibility of polarized positron beam

## Slide 18: Thank You For Your Attention !
Acknowledgement
I would like to thank all members of JLab EIC design study group and our external collaborators, especially:
  Yaroslav S. Derbenev, Vasiliy S. Morozov, Yuhong Zhang, Jefferson Lab, USA
  Desmond P. Barber, DESY/Liverpool/Cockcroft, Germany
  Anatoliy M. Kondratenko, Scientific and Technical Laboratory Zaryad, Novosibirsk, Russia
  Yury N. Filatov, Moscow Institute of Physics and Technology, Dolgoprudny Russia
This wok has been done under U.S. DOE Contract No. DE-AC05-06OR23177 and DE-AC02-06CH11357.
Notes: Title Page

## Slide 19
Back Up
Notes: Interior Page

## Slide 20: SLIM Algorithm And Spin Matching
Obtaining expressions for in an linear approximation of orbit and spin motion. For spin, the linearization assumes small angle between and at all positions in phase space so that the approximately with an assumption that . ( and are 1-turn periodic and is orthonormal.) This approximation reveals just the 1st order spin-orbit resonances and it breaks down when becomes large very close to resonances. The code SLICK (created and developed by Prof. A.W. Chao and Prof. D.P. Barber) calculates the equilibrium polarization and depolarization time under these approximations.
The combined linear orbit and spin motion is described by 8x8 transport matrices of
(, ) ()
is a symplectic matrix describing orbital motion;
describes the coupling of the spin variables (, ) to the orbit and depend on and .
matrix is the target of spin matching mechanism and can be adjusted only within linear approximation
for spin motion in the lattice design (successfully used at HERA electron ring (DESY, Germany)).
is a rotation matrix associated with describing the spin motion in the periodic reference frame.
Notes: We understand those terminologies of electron polarization quantitatively. Now we need to describe (or estimate) the electron polarization quantitatively. Two classes of computer algorithm for estimating the equilibrium polarization and lifetime: i) methods on evaluating (𝜕𝑛 ̂)/𝜕𝛿 in the D-K formula given the ring layout and magnet strengths; ii) algorithm using Monte-Carlo tracking.
Class i) methods are further divided according the degree of linearization of the spin and orbit motion, SLIM family (linearization of orbital and pin motion), SMILE (linearized orbital motion but nonlinear spin motion), SPRINT (linearized orbital motion but nonlinear spin motion). Here I briefly introduce the SLIM algorithm created by Dr. Alex Chao and Dr. Desmond Barber, which is used widely for the estimation of electron polarization under the linearization scale for the first step of polarization studies, of course here for MEIC.

## Slide 21: SLIM Algorithm (cont.)
The eigenvectors for one turn matrix can be written as
are the eigenvectors for orbital motion with eigenvalues
are the spin components of the orbit eigenvectors .
Finally, the spin-orbit coupling term can be expressed as
This is the spin-orbit coupling function used in the code SLICK (created and developed by Prof. A.W. Chao and Prof. D.P. Barber) to calculate the equilibrium polarization and depolarization time under the linear orbit and spin approximation.
Notes: The 𝑣 ⃑_𝑘 are the eigenvectors for orbital motion with eigenvaluesof 𝜆_𝑘=𝑒^(−𝑖2𝜋𝜐_𝑘 )
〖𝑣_𝑘5〗^∗ embodies the impulse perturbation to electron state due to the photon emission event. In the spin-orbit coupling terms, each term is basically the product of the sensitivity of an orbit amplitude to a change of 𝛿 and the sensitivity of 𝑛 ̂ to a change of that orbit amplitude. |𝑣_𝑘5 |^2 is the analogue of function H usually seen when using beta and dispersion functions

## Slide 22: Electron Injection And Polarimetry

## Slide 23: General Information Of Helical Dipole
The trajectories in the helical magnet is determined by the equations
, , .
The solutions of orbits are
, , ,
where is the amplitude of the particle orbit in a helical magnet.
The curvatures of the orbits in the horizontal, vertical and longitudinal direction are
, , .
The 3D curvature can be calculated through
The integral of helical field:
from Dr. Kondratenko’s thesis for protons
we can obtain for electrons
where M is the integer number of field periods,  is the spin rotation angle, Ge=0.001159652.

## Slide 24: Effects Of Helical Dipoles
Synchrotron radiation power is calculated using the following two formulas
  where , I is the beam current, B is the magnetic field, is the local radius of curvature, E is the beam energy.
Orbit excursion is calculated as the amplitude of the particle orbit in the helical magnet
where wave number , is helical magnet period, is the integer number of field period in the long helical magnet.
===>
===>

## Slide 25: Impact Of Solenoid & Helical Dipole
 | Solenoid | Helical Dipole
Synchrotron Radiation | No | Yes3
Orbit Excursion | No | Yes4
Coupling | Yes1 | No
Polarity Change Needed | Yes2 | No
Quadrupole decoupling scheme is applied in the current USR design, which occupies ~8.6m long space for each solenoid.
The solenoids have the opposite field directions in the two adjacent USRs in the same interaction region. Such an arrangement cancels the first order spin perturbation due to the non-zero integral of solenoid fields, but the polarization time may be restricted by the Sokolov-Ternov depolarization effect, in particular at higher energies.
Synchrotron radiation power should be controlled lower than 20kW/m at all energies.
Orbit excursion should be as small as possible (< a few centimeters).
Helical-dipole spin rotator ?
Comparison

## Slide 26: Effects Of Helical Dipoles
Synchrotron radiation power is calculated using the following two formulas
  where , I is the beam current, B is the magnetic field, is the local radius of curvature, E is the beam energy.
Orbit excursion is calculated as the amplitude of the particle orbit in the helical magnet
where wave number , is helical magnet period, is the integer number of field
period in the long helical magnet.
===>
===>

## Slide 27: Estimation Of Helical Dipole Effects
E | Beam Current | 1st Helical Dipole (L=20m, M=4) |  |  |  | 
 |  | Spin Rot. | BDL | B | Amp_x,y | Syn. Rad. Power
GeV | A | rad | T·m | T | cm | kW/m
3 | 3 | π/2 | 13.26 | 0.66 | 4.2 | 15.1
4.5 | 3 | π/4 | 9.31 | 0.47 | 2.0 | 16.7
6 | 2.0 | 0.62 | 8.26 | 0.41 | 1.3 | 15.5
9 | 0.4 | π/6 | 7.58 | 0.38 | 0.8 | 5.9
12 | 0.18 | 0.62 | 8.26 | 0.41 | 0.7 | 5.6
E | Beam Current | 2nd Helical Dipole (L=20m, M=4) |  |  |  | 
 |  | Spin Rot. | BDL | B | Amp_x,y | Syn. Rad. Power
GeV | A | rad | T·m | T | cm | kW/m
3 | 3 | 0 | 0 | 0 | 0 | 0
4.5 | 3 | π/2 | 13.26 | 0.66 | 2.8 | 33.8
6 | 2.0 | 1.91 | 14.67 | 0.73 | 2.3 | 49.0
9 | 0.4 | 2π/3 | 15.39 | 0.77 | 1.6 | 24.3
12 | 0.18 | 1.91 | 14.67 | 0.73 | 1.2 | 17.7