## Slide 1: An optically pumped spin-exchange polarized electron source
Munir Pirbhai

## Slide 2: Wanted: a “push-button” polarized electron source
Desired characteristics:
Operates with less stringent vacuum requirements.
Less susceptible to contaminants.

## Slide 3: Example of an atomic physics “table-top” experiment: Electron circular dichroism
Source
Target
(bromocamphor)
J. M. Dreiling, private communication.
Notes: 5 mTorr

## Slide 4: An idea for producing polarized electrons
P. S. Farago and H. Siegmann, Phys. Lett. 20, 279 (1966).
R. Krisciokaitis-Krisst et al., Nucl. Instrum. Methods 118, 157 (1974).
H.Batelaan et al., Phys. Rev. Lett. 82, 4216 (1999).
C.Bahrim et al., Phys. Rev. A 63, 042710 (2001).
Notes: What technique is used to orient the rubidium atoms? Mention that we will come back to this in more detail later.

## Slide 5: Working of the optically‐pumped spin‐exchange polarized electron source
Pump laser
Unpolarized
electrons
Rb atoms
Polarized
electrons
+ buffer gas

## Slide 6: Role of buffer gas
Minimizes diffusion
Mitigates radiation trapping
Thermalizes electrons
Increases electron effective path length
H.Batelaan et al., Phys. Rev. Lett. 82, 4216 (1999).

## Slide 7: Schematic of apparatus
A) tungsten filament; B) collision cell; C) differential pumping chamber; D) retractable electron collector; E) electron polarimeter; F) optical polarimeter; G) Faraday cup
10cm

## Slide 8: Optical layout
Pump laser
(795nm)
M
M
LP
QWP
Probe laser
M
LP
ND
Photodiode

## Slide 9: Apparatus
10cm

## Slide 10: Source: collision cell/electron gun
Collision cell
Rb reservoir
Gas inlet
Pressure gauge
Filament

## Slide 11: Optical electron polarimeter
A) entrance; B) target-gas-feed capillary; C) mounting sleeve; D) optical polarimeter; E) chamber housing electron collector and viewport; F) main vacuum chamber; G) fluorescence collection lens; H) energy-defining cylinder
T.J.Gay, J. Phys. B 16, L553 (1983).
M.Pirbhai et al., Rev. Sci. Instrum. 84, 053113 (2013).

## Slide 12: Electron optical polarimeter
Earlier optical polarimeters ~ 10-10
This device with argon gas ~ 10-8
High efficiency Mott ~ 10-4

## Slide 13: Experiments
Electron-spin reversal phenomenon
Different buffer gases
Dependence on incident electron energy

## Slide 14
Electron-spin reversal
E.B.Norrgard, D.Tupa, J.M.Dreiling, T.J.Gay, Phys. Rev. A 82, 033408 (2010).
Notes: Maybe put E. Norrgard’s reference here.

## Slide 15: Experiment 1: Electronic spin reversal
87Rb
2→1
2→2
87Rb
1→1
1→2
85Rb
3→2
3→3
85Rb
2→2
2→3
+
F = 3
I = 5/2
S = 1/2
I
F
S

## Slide 16: Experiment 1: Electronic spin reversal
87Rb
2→1
2→2
87Rb
1→1
1→2
85Rb
3→2
3→3
85Rb
2→2
2→3
+
F = 2
I = 5/2
S = 1/2
I
F
S

## Slide 17: Experiment 1: electron-spin reversal
87Rb
2→1
2→2
87Rb
1→1
1→2
85Rb
3→2
3→3
85Rb
2→2
2→3
Notes: This gives us another handle on reversing the polarization on the electron beam.

## Slide 18: Experiment 1: two ways to reverse beam polarization
Optical helicity
Pump wavelength detuning
Notes: This gives us another handle on reversing the polarization on the electron beam.

## Slide 19
Different buffer gases:
He
H2
N2
C2H4
Ei~2eV
Ei~4eV
Notes: All buffer gases are equal, but some are more equal than others.

## Slide 20: Experiment 2: performance with different buffer gases
Pe~24%; I~4μA
GaAs source on
ECD experiment
Notes: This 4 microamps with 24% polarization is now comparable to the performance of the GaAs source we get on the experiment using chiral molecules and other nasty chemicals as targets.

## Slide 21: Experiment 2: characteristics of the different buffer gases
Gas | Quenching cross-section (Å2)
Ethylene | 139
Helium | ˂˂ 1
Hydrogen | 6
Nitrogen | 58
W.Happer, Rev. Mod. Phys. 44, 169, (1972).
J.M.Warman and M.C.Sauer, J. Chem. Phys. 62, 1971 (1975).

## Slide 22
Energy dependence of Pe

## Slide 23: Experiment 3: dependence of Pe on electron energy

## Slide 24: Experiment 3: dependence of Pe on electron energy

## Slide 25: Experiment 3: temporary negative ion formation
G.J.Schulz, Phys. Rev. 116, 1141 (1959).

## Slide 26: Experiment 3: electronic excitation
A. Bogaerts, Spectrochim. Acta Part B 64, 129 (2009).

## Slide 27: Experiment 3: ionization
Y.Itikawa, J. Phys. Chem. Ref. Data 35, 31 (2006).

## Slide 28: Experiment 3: retarding field analysis
C. B. Opal et al., J. Chem. Phys. 55, 4100 (1971).
No gas
With gas

## Slide 29: Future improvements
Repump laser
Benzene as buffer gas
Higher buffer gas pressure
Rubidium dispensers
R.G.W.Norrish and W.MacF.Smith, Proc.Roy.Soc.London A176, 295 (1940).

## Slide 30
Timothy J. Gay
Paul D. Burrow
Dale Tupa (LANL)
Eric T. Litaker
Jonah Knepper
Herman Batelaan
Praise the bridge that carried you over.
— George Colman

## Slide 32: Experiment 1: Rubidium D1 transitions
D1
794.979 nm
377.11 THz
(72%)
(28%)
P. Siddons et al., J. Phys. B 41, 155004 (2008)