## Slide 1: The polarized hydrogen jet target measurements at RHIC
Andrei Poblaguev
Brookhaven National Laboratory
The RHIC/AGS Polarimetry Group:
I. Alekseev, E. Aschenauer, G. Atoian, A. Bazilevsky, A.Dion, K.O. Eyser, H. Huang, D.Kalinkin,
Y. Makdisi, A.Poblaguev, W. Schmidke, D. Smirnov, D. Svirida, K. Yip, A. Zelenski

## Slide 2
PHENIX (p)
AGS
LINAC
BOOSTER
Pol. H- Source
Solenoid Partial Siberian Snake
200 MeV Polarimeter
Helical Partial
Siberian Snake
Spin Rotators
(longitudinal polarization)
Siberian Snakes
Spin Rotators
(longitudinal polarization)
Strong AGS Snake
RHIC pC Polarimeters
Absolute Polarimeter (H jet)
STAR (p)
AGS pC Polarimeter
Spin flipper
Polarized Proton Beams at RHIC
H-Jet polarimeter: (96 channels)
- measure average (absolute) polarization of RHIC beams

## Slide 3: The Polarized H-Jet Target
separation
magnets
(sextupoles)
H2 dissociator
RF cavity
focusing
magnets
(sextupoles)
RF transitions
Holding field
magnet
recoil detectors
ToF, EREC; QREC
record beam intensity
100% eff. RF transitions
focusing high intensity
B-R polarimeter
Pjet ~ 0.92
OR
P+ OR P-
H = p+ + e-
Atomic Beam Source
Scattering chamber
Breit-Rabi Polarimeter
Ion Gage

## Slide 4
Recoil Spectrometer Measurement
Array of Si detectors measures TR & tof
of recoil particles.
Channel # corresponds to recoil angle R.
2 correlations , (TR & tof ) and (TR & R ),
to isolate the elastic process
Ch#1- 16
proton beam
Forward scattered
proton
proton target
recoil proton
R
Ch#1
#16
(Run 2004 Configuration)

## Slide 5: Running conditions (2013)
255 GeV/c proton beams.
6 detectors (98 channels)
Ran with two beam simultaneously separated vertically
by 3-4 mm dictated by the machine beam-beam
requirements.
Alpha-source runs were taken separately from physics runs.
Full waveform was recorded for every triggered event
Recoil protons were selected within energy range 1 – 5 MeV
Recoil proton asymmetry relative to the beam and jet
polarization was mesured simultaneously
aBeam = AN(t) PBeam & aJet = AN(t) PJet
PBeam = (aBeam /aJet ) × PJet

## Slide 6: Analyzing Power
Average Analyzing Power in Run 13:
Variations of the measured value of AN are less than 1%
255 GeV
pp-CNI
Used for polarization measurements
24 GeV: PRD 79, 094014(2009)
31 GeV: Preliminary
100 GeV: PLB 638 (2006) 450
250 GeV: Preliminary

## Slide 7
Polarization measurement in the H-Jet in Run 13
Fills 17201 – 17324 (Run13 Lattice)
Fills 17328 – 17601 (Run12 Lattice)
Preliminary Analysis:
Fills 17328 – 17601 (Run12 Lattice)

## Slide 8: Event Selection
To measure polarization we have to isolate elastic recoil proton:
Detected particle is proton (from the Ekin = Mpv2/2)
Missing mass cut: MX(E,) = Mp (p+p  p+X)
Actual cuts:
Time cut depending on the amplitude (energy)
Amplitude cut depending on the strip number
Waveform  Signal amplitude (A) and time (t)
Parameters α, t0, and xDL are determined in the calibration
At first approximation, calibration is not needed for the polarization measurement with H-Jet. Since effective Analyzing Power is internally measured, we may just select events from the Amplitude-Time plot.
Background may affect polarization measurement. Precise calibration is important for proper background suppression.

## Slide 9: Calibration methods used in HJet
All three methods use essentially different experimental data
Neither method allows to determine all calibration parameters α, t0, xDL
Every method combined with experimentally measured dependence
t = t(A) allows us to determine all calibration parameters α, t0, xDL.
α-particles from 241Am and 148Gd (α, xDL)
high energy (low amplitude) prompt particles (t0)
geometry based calibration (t0 and α* )

## Slide 10: Calibration using a-source
Pair of α-signals (Gd and Am) and known stopping power allows us to measure both α and xDL
Only half of detectors have Gd signal
An average dead-layer same for all Si strips is used after calibration.
Possible variation of dead-layer as well as different materials in the dead-layer are included to the estimated error of gains and dead-layer.

## Slide 11
Determination of t0 from the prompt events
Si4 all events
Amplitude selection for the prompt t0 determination.
Prompt Time should be measured with
40<A<50 cut.
A naive estimate tprompt = t0 + L/c = t0 + 2.7 ns does not work well
( a correction may be found in comparison with other methods)
Prompt RMS includes variation of delays in the strips

## Slide 12: Proton energy spectrum in elastic pp interaction
For a narrow Si strip:
For a 4.44 mm strip:
For elastic pp-interactions , the function
where A is signal amplitude, gives the image of the jet concentration along z-axis. The value of A at the maximum may be associated with a well defined (from the detector geometry) energy.
Acceptance
Jet Density
A beam gas background is expected to be the same for all strips. This background may be amplitude (energy) dependent.

## Slide 13
pp peaks (jet profile)
“flat” background
background from prompts
pp signals and backgrounds are approximately the same in all strips.
5 pp signals may be used for calibration. Other – to evaluate background
for eight (yellow) strips of the detector 3 (Fill 17600)

## Slide 14
The calibration schema
Si4
t0 is measured in a model independent (almost) way, without any knowledge about gain and dead-layer.
If we measure the dependence t=t(A) , then for every amplitude we may calculate the energy:
Gain α and dead-layer d are only one of the possible parameterizations of t=t(A)
Accuracy of the t0 determination is crucial for the energy calibration.

## Slide 15: First Results (Run 17600)
Very poor consistency between two method of determination of t0.
Results for different beam/side strips are shown by different colors.
A geometrical alignment (in software) is needed !

## Slide 16
Geometrical Alignment
Coordinate selection: x-axis goes through centers of detectos 2 and 5
z-axis perpendicular to x (and horizontal)
Alignment parameters: z1, z3, z4, z6, zJet
 = (B+Y)/2
 = B-Y
Holding Field Correction:
Calculation:
Calculation may be inaccurate. We should determine b from the fit. b is strongly correlated with  .

## Slide 17
Results After Alignment
Contribution to the energy calibration:
 |  | Fill 17247 | Fill 17600
z1 | (mm) | 0.17 ± 0.24 | 0.33 ± 0.16
z3 | (mm) | -0.09 ± 0.27 | 0.07 ± 0.17
z4 | (mm) | -0.38 ± 0.22 | -0.36 ± 0.14
z6 | (mm) | -0.64 ± 0.22 | -0.54 ± 0.24
zJet | (mm) | 0.13 ± 0.11 | -0.05 ± 0.07
 | (mrad) | 0.35 ± 0.60 | -0.10 ± 0.39
 | (mrad) | 0.07 ± 0.18 | -0.04 ± 0.12
b | (MeV cm) | 9.7 ± 2.8 | 12.4 ± 1.9
Alignment results
for March 25 and June 8 are consistent
Accuracy of the t0 determination:

## Slide 18: Comparison α- and geometry based calibration
If Ageom is mean proton amplitude, Egeom is energy corresponding to it, and Eα(Ageom) is energy calculated using α-caliration then the value of
allows us to compare two calibrations directly
No dependence on signal amplitude is observed.
The consistency of the calibrations may be improved if the dead-layer will be treated separetely for each detector.
Energy calibration is controlled at ~ 1% level.

## Slide 19
t0 dependence on amplitude
Measured time
Time-of-Flight
No indication that t is associated with it.
Signal waveform depends on amplitude.
This dependence may be parameterized:
t (A) ≈ 0.005 A

## Slide 20
The formula
Is applicable only to first two processes
Systematic Errors in the H-Jet Measurements
Processes detected by the polarimeter
Elastic scattering
Inelastic scattering
Molecular hydrogen in jet
Beam gas background

## Slide 21
The Jet Polarization
There are 2 hydrogen components in the jet:
- atomic with (measured) polarization PBR≈96%
- molecular (unpolarized)
The admixture of molecular hydrogen atomic equivale
ε≈ 3%
was measured in 2004 and 2005 with an error of about 2 %.
The average polarization
Pjet = (1- ε) ×PBR
should be used in analysis
In ONLINE analysis the value of Pjet = 92% was used.

## Slide 22
Beam gas background
Background level : r ~ 5%
For the Jet asymmetry measurements α=0 (no dependence on Jet polarization)
For the Beam asymmetry measurements α is unknow.
For beam gas protons only background α=1
Some previous experimental estimates gave α≈0.

## Slide 23
Estimation of background effect. Method I
Rate per bunch
All strips
Yellow side
Blue side
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
+
+
+
+
-
-
-
-
-
+
+
+
+
+
+
-
+
-
-
-
-
Abort gaps
Background events in “blue strips”
Background events in “yellow strips”
Bunches with a single beam (abort gaps) may be employed to understand background
Single beam stores (blue and yellow) at the end of Run 13
The method is under development.

## Slide 24
Estimation of background effect. Method II
Two methods for background subtraction
- from the fit
- average background
The method is not verified yet

## Slide 25: Summary
H-Jet polarimeter provide reliable measurements of the average beam polarizations at RHIC.
Several calibration methods were developed which allow us to monitor energy calibration with a percent accuracy as well as to make a precise alignment of the detectors.
Study of background due to the beam gas is underway
Molecular hydrogen in the Jet gives the largest uncertainty in the polarization measurements.
For future we are considering replacing of the WFD system from the old 8-bit CAMAC based to the recently developed JLab’s 250 MHz VME-based.
We are developing new Si detectors to increase acceptance and energy range.

## Slide 26
Backup

## Slide 27
pp peaks (jet profile)
“flat” background
background from prompts
pp signals and backgrounds are approximately the same in all strips.
5 pp signals may be used for calibration. Other – to evaluate background
for eight (yellow) strips of the detector 1 (Fill 17273)

## Slide 28
pp peaks (jet profile)
“flat” background
background from prompts
pp signals and backgrounds are approximately the same in all strips.
5 pp signals may be used for calibration. Other – to evaluate background
for eight (yellow) strips of the detector 1 (Fill 17600)

## Slide 29: Background Evaluation
The algorithm is satisfactory for the calibration purposes.
To study background asymmetry, an improvement is needed.

## Slide 30
Systematic Errors in the H-Jet Measurements
Jet Polarization: there are 2 hydrogen components in the jet:
- atomic with (measured) polarization PBR≈96%
- molecular (unpolarized)
The admixture of molecular hydrogen was measured to be ε≈ 3% but, but systematic errors of this measurement is not well known. The average polarization
Pjet = (1- ε) ×PBR should be used in analysis
Background:
r ~ 5% is background level
For Jet asymmetry α=0. For beam asymmetry α is unknown and may be as large as 1 (e.g for beam gas protons).
(some previous experimental estimates gave α≈0)
In ONLINE analysis the value of Pjet = 92% was used.

## Slide 31: Detector 1 after background subtraction
Background subtraction works !
Inelastic pp ?
All n(z) profiles must be the same (if gain and cuts are the same)

## Slide 32: Analyzing Power
● 2011
● 2009 (blue)
● 2009 (yellow)
100 GeV/c
● 2004
● 2011
● 2012
24 GeV/c
Average Analyzing Power in Run 13:
Variations of the measured value of AN are less than 1%
255 GeV
pp-CNI
Used for polarization measurements
24 GeV: PRD 79, 094014(2009)
31 GeV: Preliminary
100 GeV: PLB 638 (2006) 450
250 GeV: Preliminary

## Slide 33
Systematic Errors in the H-Jet Measurements
Jet Polarization: there are 2 hydrogen components in the jet:
- atomic with (measured) polarization PBR≈96%
- molecular (unpolarized)
The admixture of molecular hydrogen was measured to be ε≈ 3% but, but systematic errors of this measurement is not well known. The average polarization
Pjet = (1- ε) ×PBR should be used in analysis
Background:
r ~ 5% is background level
For Jet asymmetry α=0. For beam asymmetry α is unknown and may be as large as 1 (e.g for beam gas protons).
(some previous experimental estimates gave α≈0)
In ONLINE analysis the value of Pjet = 92% was used.

## Slide 34
Estimation of background effect. Method I
Oleg Eyser:
Bunches with a single beam (abort gaps) may be employed to understand background
Single beam stores (blue and yellow) at the end of Run 13
The method is under development.
4.4 mm

## Slide 35: Summary
.