## Slide 1
Long term performance of the COSY/Jülich polarized ion source
September 13, 2013 | Ralf Gebel
Institute for Nuclear Physics (IKP-4/COSY) Jülich Centre for Hadron Physics (JCHP)

## Slide 2: Outline
Introduction
Status
Performance milestones
Details and current investigations
Outlook

## Slide 3: Introduction: COSY
Cooler and storage ring for (polarized) protons and deuterons
p = 0.3 – 3.7 GeV/c
Phase space
cooled internal &
extracted beams
Injector
cyclotron
COSY
e-Cooler(s*)
(*) The 2 MeV e-cooler has been installed in 2013 … and soon a superconducting snake: 1m, 5 T, full ramp in 30 s

## Slide 4: Introduction: COSY‘s Injector
AEG cyclotron
AEG design
Request for quote: 1961
First internal beam: 1968
Upgrade for COSY: 1990
Pole diameter 3.3 m / 700 t iron
<B>max =1.35 T Bhill = 1.97 T
20 – 30 MHz (h=3)
22.5-45 MeV/A
2-4.5 keV/A injection
3 ion sources (2 multicusp +pol. CBS)
routinely 45 MeV H- and 75 MeV D- for COSY with 20 ms stripping injection/cycle

## Slide 5: Ion Sources at the Injector Cyclotron
Wien filter
Lamb shift
Injection energy: 4.5 +/- 0.02 keV/u
Acceptance: 150 µm rad
Transmission: <0.1

## Slide 6
Status: COSY and Cyclotron Operation
Availability (Up time) of the injector cyclotron Distribution of beam species
accumulated hours

## Slide 7: Status: Statistics 2000 –2012
Delivered beam species COSY’s availability: > 92% (average)
 | Protons | Deuterons | pol. Protons | pol. Deuterons
beam hours |  |  |  | 
since 2000 | 52800 | 6600 | 23000 | 11700
 | 56% | 7% | 24% | 12%
sum | ~59400 h |  | ~34700 h | 
average/ year | 4570 hours/year |  | 2670 hours/year | 

## Slide 8
Status: run plan 2013

## Slide 9: COSY state September 2013: 0.97 GeV/c electron cooled polarized deuterons
left/right asymmetries
Polarized sources delivers Pz=(+/-/0)
number of particles

## Slide 10: „Current“ COSY state: 0.97 GeV/c electron cooled polarized deuterons
particle number
beam current
number of particles

## Slide 11: COSY‘s Polarized Ion Source
Charge exchange reaction
H0(D0) + Cs0  H-(D-) + Cs+
RF discharge
Thermal ionizer
38 K
1150 K
550 K
Ref.: Haeberli , NIM 62(1968)

## Slide 12: COSY‘s Polarized Ion Source
About 6 m from the pulsed ABS to the Cs ionizer

## Slide 13: Performance (Reference values 1)
Beam current at the source exit*
*compare to routine COSY fill of a few 1010 protons or deuterons
(space charge limit of about 1011)
Polarization inside COSY
Data from Exp. EDDA
(pp – elastic scattering)
Pavg = (91.4  2.2 ) %

## Slide 14: Performance (Reference values 2)
With 6 pmA Cs @ 50 kV
Gradient voltage -> energy spread
High polarization is preferred
Magnetic field -> emittance growth

## Slide 15: Performance (Reference values 3)
unpolarized deuterons
switching to polarized deuterons
best values for COSY: 35 mA unpol. D and 6 mA pol. D

## Slide 16: Performance Milestones
1993 Installation
1994 ABS: Pulsed operation
Cs Ionizer: Prototype replacement
1998 ABS: PM sextupoles
Cs dispenser; electron beam heating
2000 Pulsed Cs Ionizer first routine operation for COSY experiments
2001 H- extraction with EM-dipole
D- extraction with PM-EM-dipole
2003 routine D- operation for COSY
ABS: Pulsed mode optimization (with A.S.Belov)
2007 Polarimeter improvements
        Breit Rabi
        Lambshift
        45 MeV
2012 New Cs dispenser generation for ionizer Laser applications

## Slide 17: Keep Performance
Identify and replace weak components
Get spares (build or inherit (EDDA ABT))
  Dissociators (> 4 + prototypes)
  Transition units (9 + spare cavities)
  Cs ionizers (3 + 6 ovens + N W-ionizer)
  Neutralizers (3 cells, > 3 oven units, …)
  …
Improved diagnostics (Viewer,Polarimeter,…)
Test facilities
New cleaning methods

## Slide 18: Cs Ionizer development
DC version (2 prototypes)
Version 2 features
Reservoir under vacuum
Short transfer line
Improved positioning
Pulsed version (3 identical inserts)
with separation of heater and reservoir
FZJ made tungsten ionizer
Electron beam heating
1 of 3 Cs ionizers, and within the external test facility
Prototype 1

## Slide 19: Prototype replacement (cw)
S. Lemaitre’s and R. Reckenfelderbäumer’s Ph.D. theses NIM A 408, 345 (1998)
External oven
Resistively heated dispenser
Long heated transfer tube
Heater failure

## Slide 20: Intermediate Cs Ionizers
Electron beam heated, improved thermal design

## Slide 21: Current: pulsed Ionizer

## Slide 22: Examples for Cs+ pulses
5.5 mA
20 ms
55°C
60°C
65°C
-4 kV
-5 kV
-6 kV
-7 kV
-7.5 kV
0
4
8
12
mA

## Slide 23: FZJ made Tungsten Ionizer
Similar to dispenser cathode for electron guns, but with:
Electron beam welded permeable tungsten - molybdenum (TZM) connection
Capability to allow >200 W heating to over 1100°C (e.g. for conditioning)
Optional special shaping of the emitter surface by spark erosion
Quality control and assurance of all production steps
Experienced Issues, with consequences for reproducibility and performance:
Porosity variation, contamination, surface quality, cracks, welding quality….
> 100 samples tested
New, improved samples available!

## Slide 24: Successful Recovery with IR Laser
Application samples:
Tungsten, Mo, Ti, Steel …
Speed: up to several cm²/s
20 mm
Cs Ionizer
Cs Extraction
From RF Transition
Treated dispensers behave unused!

## Slide 25: Micro second laser cleaning
Parameter | P20 (Titan) | P103 / P104 (SS) | Probe 3 (W)
Puls frequency / kHz | 200 | 110 200 (2x) | 110
velocity area rate / cm²/s | 6,4 | 1,9 (1x) 1,0 (2x) | 2,5
Parameter studies

## Slide 26: Femtosecond laser micro sintering
R. Ebert et al., University of Applied Science, Laser Institute, 17 Technikumplatz, 09648 Mittweida, Germany; Laser Processing of Tungsten Powder with Femtosecond Laser Radiation
Proceedings of LPM2010 - the 11th International Symposium on Laser Precision Microfabrication 1
Tungsten dispenser disks:
sintered to desired shape and and density
sample disks arrived at FZJ: promising …

## Slide 27: Cs beam diagnostic tools
A set of computer controlled wire scanners
for Cs+/o diagnosis
to judge the beam and the ionizer quality
to optimize Cs+/o transmission
space charge compensation by adding Argon

## Slide 28: Source watching

## Slide 29
Graphite collimator (15 mm)
Cs
Cs beam (deflected on purpose)

## Slide 30: Neutral Cs beam in the ABS

## Slide 31: Neutral Cs beam in the ABS
Cs beam off (Button glows)
Cs beam on (check for focusing)
A moveable viewer plate (45 degree) allows quick Cs beam alignment.

## Slide 32: Neutralizer
Improved geometry
Modular design with exchangeable flapper unit
Cs reservoir: 45 - 60 g
Exchange interval: > 2 years (> 5000 hours beam)
Neutralization > 90%
Vapor cell (32° C)
(water, double wall)
Magnetic flapper valve
Shielded Cs oven (278° C)
50 mm

## Slide 33: Replacement of Deflectors
New chamber with
  E-deflector for Cs+
  Water cooled EM-PM-Hybrid for H-/D-
Improved cooling (to trap Cs)

## Slide 34: PM sextupoles
EM diameter 220 mm
PM diameter 80 mm
M. Altmeier’s and O. Felden’s Ph.D. theses NIM A 626, 117 (1997)

## Slide 35: ABS: RF Transitions
For Protons:
λ/2 – 1.43 GHz
Q: 800 - 1200
For Deuterons: tuneable!
λ/4 – 0.3 – 0.45 GHz
Q: 800 - 1100

## Slide 36: Breit Rabi-Polarimeter
RFT 3 @ 5.65 MHz (D)
RFT 2 @ 328 MHz (D)
Magnetic field
intensity
intensity
intensity
Magnetic field
Magnetic field
RFT 3 @ 5.65 MHz (H)

## Slide 37: Lambshift-Polarimeter
Usable for tuning
Double stripping of H-/D-
Neutralization of p/d
Spin filter

## Slide 38: 45 MeV Polarimeters
Calibration

## Slide 39: 45 MeV-Polarimeter (Upgrade)
12 Plastic scintillators (NE110)
More statistics
Similar resolution
Now C and CH2 targets
With CH2 kinematic dp coincidences
allow fast electronics / 100 MHz
Cross calibration with NaI and C Target
Pol. H- on C target
Pol. D- on CH2 target

## Slide 40: 45 MeV Polarimeter
Several Carbon targets (C)
Chromox viewer
pC elastic
NaI scintillator @ 52.5° (Lab)
Amplifier & TSCA for MHz Counter
Pulse height analysis

## Slide 41: Monitoring Beam Asymmetries
Solenoid reversal
Transition unit retuned
11 days of deuteron beam

## Slide 42: Testbench for Atomic beam parts
Equipment for neutral beams:
Quadrupole mass spectrometer,
TOF spectrometer,
Compression tubes,
Diaphragms, Chopper, Scanner etc.
For:
Intensity
Density, profiles
Velocity distribution
Used for offline tests of e.g. transition units
  cw operation: 4x1016 (initial CBS)
  Pulsed: 7.5x1016 (COSY operation)
  Improved: 11x1016 with spare PM hexapoles (EDDA)

## Slide 43: Pulsed ABS development
Optimized design for pulsed operation
Improved performance: doubles density for free atomic beam better beam cooling higher gas flux up to 3 kW RF power

## Slide 44: Outlook
R&D for Hadron Storage Rings
Topics (with FZJ as leading lab)
(polarized) Ion sources for hadron storage rings
  Assure high intensity beams for COSY/JEDI
  Enable experiments at e.g. FAIR with polarized beams
Combined electrostatic and magnetic deflectors
  Search for an electric dipole moment in p, d and He3
High energy beam cooling and broad band stochastic cooling
  Electron cooling up to COSY’s maximum momentum
  Electron cooling for HESR
  Fast stochastic cooling at different energies

## Slide 45: Thank you for your attention