## Slide 1: Boosting Deuteron Polarization in HD Targets: Experience of moving spins between H and D with RF methods during the E06-101 experiment at Jefferson Lab
Xiangdong Wei
Thomas Jefferson National Accelerator Facility
The XVth International Workshop on Polarized Sources, Targets and Polarimetry (PTSP 2013)
University of Virginia, Charlottesville, Virginia, USA
September 9-13, 2013
H
D
ice

## Slide 2: Collaborators
Jefferson Lab
X. Wei, C. Bass, A. Deur, G. Dezern, T. Kageya, M.M. Lowry,
A. M. Sandorfi and R. Teachey
Universita di Roma “Tor Vergata” and INFN-Sezione di Roma2
A. D'Angelo
Blaise Pascal University
V. Laine
James Madison University
C.S. Whisnant
H
D
ice

## Slide 3: Topics
Target Life-Cycle
Spin Manipulation Methods
Experimental Setup
Target Performance During E06-101 Experiment
Summary
H
D
ice

## Slide 4: Topics
Target Life-Cycle
Spin Manipulation Methods
Experimental Setup
Target Performance During E06-101 Experiment
Summary
H
D
ice

## Slide 5: HD Target Life Cycle
Gas Handling
Gas recovery
Gas Storage
HD purification (JMU)
Gas analysis (JMU, Rome2)
Target Production
Condensing
Calibrating
Polarizing
Aging
Experiment
(Spin Transferring)
eHD, gHD
(Spin Flipping)
(Field Rotating)
H
D
ice
See Lowry’s Talk
See Steve Whisnant’s Talk

## Slide 6: Topics
Target Life-Cycle
Spin Manipulation Methods
Experimental Setup
Target Performance During E06-101 Experiment
Summary
H
D
ice

## Slide 7: Polarize HD with High Field and Low Temp. (Brute Force)
H
D
ice
Maximum for current setup
(15T and 10 mK)
I=1/2 for H and 1 for D
Can PD be improved?
Yes.
In reality, typically
60% for H and 15% for D

## Slide 8: Spin Manipulation Methods
Adiabatically rotating magnetic field direction
  Using both transverse and axial magnets, this operation is straight forward and quick, as long as the field rotation rate is much slower than the Lamar Frequencies of H and D at the lowest field, and the T1s are much longer than the rotation time.
  Typical scales: T1 ~months;
  rotation time ~minutes;
  NMR frequency ~300kHz for D and ~2MHz for H
  @0.0600T
  Polarization amplitudes stay the same <=> H &D rotate together.
H
D
ice
+B
+B
-B

## Slide 9: Spin Manipulation Methods
2. Adiabatically flipping spins of H or D with RF
  Nearly 100% efficiency for H and 70% for D so far.
    Could be improved: uniformed RF field, stable power supply...
  Moderate RF power required (~10mW with non-tuned coils).
  Can be used with higher holding field.
H
D
ice
mD=+1
mD=0
mD=-1
mH=-1/2
mH=+1/2
PH
PD
Zeeman Levels of HD
Induce “allowed” transitions with RF
---flipping H
=42.5776MHz/T
---flipping D
=6.53359MHz/T

## Slide 10: Spin Manipulation Methods
H
D
ice
3. Transferring polarizations between H and D in different molecules
Radiated with RF: PH PD
mD=+1
mD=0
mD=-1
mH=-1/2
mH=+1/2
PH
PD
Zeeman Levels of HD
Induce “forbidden” transitions with RF
)
)

## Slide 11: Transferring polarizations
H
D
ice
H0: external magnetic field
r: the distance between H and D in different molecules
θ and φ: polar angles defined by H0.
The RF induced polarization transfer efficiency
H1 : coil generated RF field
Running at low DC field (H0) with high power RF (H1)
Circuit tuning needed to reduce heat load to fridge
Spin Dipole coupling between H and D in adjacent molecules
A. Abragam, Principles of Nuclear Magnetism, p395, (1983)
A. Honig and H. Mano, Phys. Rev. B 14, V14, vol. 5, 1858 (1976)

## Slide 12: FAFP vs. SFP
H
D
ice
FAFP-Flip entire population between levels
  εmax=100% (only if everything listed below works)
  High power RF (H1 ~ gauss)
    partial flip => low net polarization
    Watts of RF heats up fridge. Needs uniform RF field.
  Monotonic field sweep (field jitter hurts, reduces ε)..
  One chance only (available spins reduced after each operation).
  Achieved with 1 cc test target.
  NOT EASY for large target with limited cooling power and space.
SFP-Multi FAFP until population on connected levels are equalized
  ε=50% is guaranteed (it’s also the maximum)
  Fridge cold can handle the “low” RF power.
  Field and frequency jitter helps; Jittered field and modulated RF results in multiple transfers per sweep higher ε
  keep sweepings until no net spin transfer.
  Easy to achieve Used During E06-101 Experiment
  but εmax=50%

## Slide 13: Topics
Target Life-Cycle
Spin Manipulation Methods
Experimental Setup
Target Performance During E06-101 Experiment
Summary
H
D
ice

## Slide 14: Experimental Setup
NMR Coils:
  A pair of 8-post ”Birdcage” coils was utilized in HDice to improve H1 homogenty to ~10%.
Circuit Tuning:
  Cparallel was connected to the transmitter outside IBC, and Cseries was used to isolate the output impedence of RF amplifier.
  target heating under control;
  system tunned at off-resonance field.
  Circuit simulation used as the guide
  for fine tuning.
RF Power:
  A computer controlled RF switch/attenuation box was built.
  An 110W RF amplfier was added
  into the NMR spectrometer.
H
D
ice
HD
coils
ICs ICp ICoil
circuit
I(A) vs. f(MHz) in various components

## Slide 15: Operation: G-14 Run at Hall-B
H
D
ice
HDIBC in Hall B


## Slide 16: Topics
Target Life-Cycle
Spin Manipulation Methods
Experimental Setup
Target Performance During E06-101 Experiment
Summary
H
D
ice

## Slide 17: SFP Results during G-14 Run
H
D
ice

## Slide 18: Target Performance during G-14 Run
H
D
ice
HDice targets used in frozen spin mode during E06-101/g14 run. Relaxation times were longer than a year at B=0.9T and T<100mK .
RF H flip
Erase H
Field rotation
Pseudo
quench
Field rotation
Beam steering
H flip caused partial FAFP
FAFP H=>D
Quench
FAFP H=>D
Field rotation
RF H flip

## Slide 19: On-going Analysis for G-14 Run
“Empty” (red)
H
D
ice
1st look at data vertex projection
“Full” (blue)

## Slide 20: On-going Analysis for G-14 Run
“Empty” (red)
H
D
ice
1st look at data vertex projection
“Full” (blue)
eg: γn => π–p
E
P(D) = 27%
~ 10% of g14 data set
(T.Kageya, NSTAR’13)
*

## Slide 21: Summary
Methods of manipulating spins in HDice targets have been successfully implemented during the E06-101 run in CLAS.
Polarizations of H and D can be transferred back and forth.
More improvements can be done in the future to increase the spin transfer efficiency.
E06-101/g14 data from polarized D, following SFP, now under analysis.
These demonstrate a large potential for solid HD for photon experiments.
H
D
ice